## Slide 1: Short Field Operations
Cessna 172 (160 HP)
Runway: 3750 ft
Density Altitude: 6000 ft
Tailwind Scenario Included

## Slide 2: Objective
Understand performance limits and safe operation for short-field takeoff and landing.
C172 160 HP
Normally aspirated
Performance sensitive to DA and weight
Consider this Aircraft

## Slide 3: Airport Environment
Runway Length: 3750 ft
High elevation → 6000 ft DA
Reduced air density
Density Altitude Effects
Reduced engine power
Reduced propeller efficiency
Reduced lift

## Slide 4: Weight Considerations
Higher weight increases takeoff roll
Reduces climb rate
Increases landing distance
Wind Components
Headwind reduces distance
Tailwind increases distance significantly

## Slide 5: Takeoff Technique
Full power before brake release
Short-field rotation speed
Climb at Vx

## Slide 6: Takeoff Risk Factors
High DA
Tailwind
Obstacles
Overweight aircraft

## Slide 7
Takeoff Profile Comparison

## Slide 8: Landing Technique
Stabilized approach
Full flaps
Aim point control
Maximum braking
Landing Risk Factors
Tailwind increases groundspeed
Longer float distance
Reduced stopping margin

## Slide 9
Approach Profile Comparison

## Slide 10: Mitigation Strategies
Reduce weight
Fly early morning
Use headwind runway
Abort if needed
Tailwind Impact
10 kt tailwind can increase distances by 20–40% or more

## Slide 11: Go/No-Go Decision
Compare required vs available runway
Maintain safety margin
Consider alternates

## Slide 12: Common Pilot Errors
Improper speed control
Late rotation
Floating on landing

## Slide 13: Discussion
Short-field ops require planning
Tailwinds greatly increase risk
Use conservative decision-making
Summary